## Slide 1: Standards and Guidelines for the statistical treatment of PT data

## Slide 2
Standards and guidelines for providing PT / EQA schemes
ISO 13528:2022 - Statistical Methods for use in Proficiency Testing by Interlaboratory comparisons
IUPAC Technical Report 1/2006 - The International Harmonized Protocol for the Proficiency Testing of Analytical Chemistry Laboratories
ISO/TS 20612:2007 - Water Quality – Interlaboratory comparisons for proficiency testing of analytical chemistry laboratories
ISO/IEC 17043:2023 - Conformity Assessment – General Requirements for Proficiency Testing

## Slide 3
Standards and guidelines for providing PT / EQA schemes
e) ISO 17034:2016 - General requirements for the competence of reference material producers
f) ISO-Guide 35: 2017 - Reference materials – General and statistical principle for certification
g) ISO 5725-1 to -6 - Accuracy (trueness and precision) of measurement methods and results
h) ISO 22117 - Microbiology of the food chain — Specific requirements and guidance for proficiency testing by interlaboratory comparison

## Slide 4
ISO 13528:2022 - Statistical Methods for use in Proficiency Testing by Interlaboratory comparisons
5 ways to determine the Assigned Value with more
emphasis on its uncertainty
Formulation, certified reference material, results from one laboratory, consensus from expert laboratories, consensus from participants
5 ways to determine the SDPA
perception of experts, by experience from prom previous PT rounds, from a general model, from results of a precision experiment, from data in a round of a PT scheme
7 ways to report Performance statistics
Deviation, percent deviation, z-scores, En-numbers, z’-scores, Zeta-scores, PA score

## Slide 5
ISO 13528:2022 - Statistical Methods for use in Proficiency Testing by Interlaboratory comparisons
Preferred statistical method for the calculation of consensus mean and standard deviation: Algorithm A. Described in Annex C (normative) and also in ISO 5725-5:1998
but also allowed: Other calculation methods, provided that they have a sound statistical basis

## Slide 6
IUPAC Technical Report 1/2006 - The International Harmonized Protocol for the Proficiency Testing of Analytical Chemistry Laboratories
Several ways to determine Assigned Value, but the provider must report an uncertainty to the participants
for calculation of consensus mean Alg. A (called H15 here) is recommended, but with a check, if the distribution is unimodal
Performance statistics - only the use of z-scores is recommended
Determination of the SDPA - Only value determined by fitness-for-purpose is recommended.

## Slide 7
ISO/IEC 17043: 2023 -– ANNEX B – STATISTICAL METHODS FOR PT (Informative)
  B.1. General
  B.2 Assessment of PT item homogeneity & stability
  B.3 Determination of the Assigned Value and its uncertainty
  B.4 .1 Calculation of Performance statistics - Performance for quantitative results
  B.4.2 Calculation of performance statistics - Performance for nominal and ordinal results
  B.5 Evaluation of performance